Energy Research Partnership

AN ECONOMIC VALUE ASSESSMENT OF LOW CARBON PATHWAYS (EVAP)

Helen K Thomas, January 2015

## The Energy Research Partnership

The Energy Research Partnership is a high-level forum bringing together key stakeholders and funders of energy research, development, demonstration and deployment in Government, industry and academia, plus other interested bodies, to identify and work together towards shared goals.

The Partnership has been designed to give strategic direction to UK energy innovation, seeking to influence the development of new technologies and enabling timely, focussed investments to be made. It does this by (i) influencing members in their respective individual roles and capacities and (ii) communicating views more widely to other stakeholders and decision makers as appropriate. ERP’s remit covers the whole energy system, including supply (nuclear, fossil fuels, renewables), infrastructure, and the demand side (built environment, energy efficiency, transport).

ERP is currently co-chaired by John Loughhead, Chief Scientific Advisor at the Department of Energy and Climate Change and Dr Keith MacLean, formerly SSE. A small in-house team provides independent and rigorous analysis to underpin ERP’s work. ERP is supported through members’ contributions.

Co-Chairs

Prof. John Loughhead 	Chief Scientific Advisor 	DECC

Dr Keith MacLean 	Independent Co-chair 	(formerly) SSE

Members

Dr Julian Allwood 	Reader in Engineering 	University of Cambridge

Carl Arntzen	Managing Director	Bosch Thermotechnology Ltd

Dr Peter Bance 	Entrepreneur in Residence 	Origami Energy Ltd

Dr Masao Chaki	Chief Researcher	Hitachi Europe Ltd

Dr David Clarke FREng 	Chief Executive 	Energy Technologies Institute

Tom Delay 	Chief Executive 	Carbon Trust

Peter Emery 	Production Director 	Drax Power Limited

Bob Sorrell	VP for Public Partnerships 	BP International Limited

Angus Gillespie 	Vice President CO2 	Shell Int’l Petroleum Co. Ltd

Martin Grant 	Chief Executive Officer - Energy 	WS Atkins PLC

Derek Grieve	Exec Leader – Systems & Projects Eng	GE Energy Power Conversion

Dame Sue Ion FREng 	Nuclear Expert	Royal Academy of Engineering

Prof Neville Jackson FREng 	Chief Technology & Innovation Officer 	Ricardo UK Ltd

Maggie McGinlay	Director, Energy & Clean Technology	 Scottish Enterprise

Jim Watson 	Researcg Director 	UK Energy Research Centre

Dr Ron Loveland 	Energy Advisor to Welsh Government 	Welsh Government

Duncan McLaren 	Advisor 	Friends of the Earth, UK

Prof John Miles FREng 	Director & Prof of Energy Strategy 	Arup / Cambridge University

Jonathan Yewdall 	Assistant Director, Green Growth 	BIS

Rob Saunders 	Head of Energy 	InnovateUK

Philip Sellwood	Chief Executive Officer	Energy Saving Trust

Miles Elsden 	Acting Chief Scientific Advisor 	DfT

Stephen Trotter 	MD Power Systems UK & Ireland 	ABB Limited

Prof. Philip Nelson 	Chief Executive Officer 	EPSRC

Nick Winser FREng 	            Executive Director, Transmission 	          National Grid

## ERP reports

ERP Reports provide an overarching insight into the challenges for low-carbon technologies and associated energy system issues. Using the expertise of the ERP membership and wider stakeholder engagement, each report identifies the challenges for a particular cross-cutting issue, the state-of-the-art in addressing these challenges and the organisational landscape (including funding and RD&D) active in the area. The work seeks to identify critical gaps in activities that will prevent key low-carbon technologies from reaching their full potential and makes recommendations for investors and Government to address these gaps.

The views are not the official point of view of any organisation or individual and do not constitute government policy.

Lead Analyst

Helen K Thomas	Executive Researcher	Energy Research Partnership

Steering Group

Chris Pook (Chair)	Deputy Director, Green Economy	BIS

Tom Delay	Chief Executive	Carbon Trust

Rob Saunders	Head of Energy	InnovateUK

Will Lecky 	Economic Adviser	DECC

James Bolton	Economic Advisor	BIS

Aftab Malik	Assistant Economist	BIS

Eric Ling	Senior Analyst	CCC

Kenny Richmond	Head of Economics	Scottish Enterprise

Emma Edworthy	Head of Regulated Markets	Welsh Government

We would like to thank all those who helped inform this work, including Steering Group Members and their colleagues, plus the wide range of experts from relevant modelling, pathway and scenario teams who assisted with the collation of information for this work.

Please contact Helen K Thomas for information: (helen.thomas@erpuk.org).

## Summary

Existing works on low carbon pathways and policies have focused on ‘the energy trilemma’: cost of energy, security of supply and carbon emissions, often with a significant emphasis on cost effectiveness. In particular, importance has been placed on achieving the lowest costs in the short-term, with decreasing costs in the long-term.

An area that has been relatively neglected within the development of pathways and scenarios (and related models) is the value and impact on economic growth (measured in GDP/GVA), and analysis of other socio-economic effects, including at regional levels. Reasons for this relate to current modelling interests and capabilities, and a lack of existing ‘top-down’ or ‘spatial’ models utilised in the UK.

It is well known and accepted that economic and socio-economic impacts can be intangible and complex to measure and define, but there are some existing UK models that can and do assess them.

This paper addresses the issue of how the UK currently considers and assesses economic impacts and benefits within five of the UK’s major pathway and scenario works. It additionally considers modelling capabilities (now and in future) and highlights other relevant models or works that can assist with analysis in this area. Works assessed within this paper are:  1) CCC’s 4th Carbon Budget Review, 2) DECC’s 2050 Pathways/Calculator & Analysis (with some extra consideration of the Dynamic Dispatch (DDM) model), 3) ETI’s ESME model, 4) National Grid’s Future Energy Scenarios (RESOM model) and 5) the MARKAL ELASTIC DEMAND model used to inform two of UKERC’s Energy 2050 scenario works. The work additionally considers the MARKAL-MACRO and Cambridge Econometrics’ MDM-E3 models.

The paper concludes by making recommendations for further analysis of current modelling capabilities to assess these impacts, particularly within pathway and scenario works. The integration and utilisation of a wider range of existing models is recommended, to help inform policy from both a top-down and bottom-up perspective of the energy system.

## Key Insights

- Assessments of economic growth and job creation within low carbon pathways have been relatively neglected, although it is accepted that these are complex to measure and define. Current modelling types and approaches tend to focus on 1) cost-optimisation and 2) achieving the carbon targets. There is also a lack of clarity regarding input assumptions used.

- Many works are not designed to make these assessments (it is not within their remit) and incorporating this type of analysis within the models assessed is seen as unfeasible. Impacts on a regional level within the UK (Scotland, England, Wales etc.) are complex to capture and are therefore rarely assessed.

- The type and limited number of macro-economic ‘top-down’ energy models being utilised currently constrains the range and reliability of assessments informing policy. Although these models exist (e.g. the Cambridge Econometrics’ MDM-E3), many are not set up to assess the economic value of low carbon pathways and the range of economic and socio-economic impacts of interest to policy-makers.

- There is a level of uncertainty regarding current and future modelling capabilities (models are designed for a specific purpose and are not always adapted) and a range of opinions as to whether these assessments should be included within pathway and scenario works.

- Where economic impacts such as effects on jobs, supply chains and local GDP are assessed, they are often discussed within texts in a general and qualitative fashion. Works that previously carried out these assessments have adopted other, less detailed approaches, or have reduced this type of analysis substantially. This is largely to avoid introducing further uncertainty amongst input assumptions or because research interests lie elsewhere.

- It is possible to combine model types to enable economic and socio-economic analysis, as long as the aims are well defined and modelling limitations are made clear. More could be done to integrate modelling of low carbon pathways with whole economy or ‘top down’ models.

- Examining the flows of economic benefits inside and outside of the UK is complex to assess. However ongoing analyses to provide to understand this and provide better estimations of the UK’s ability to capture value from supply chains would be beneficial.

## Recommendations

This study has looked at a variety of models and criteria used to make judgements about future low carbon pathways and potential benefits to the UK. It is clear that further work is required to better understand the full range of models available in government, industry and academia to support this assessment, their limitations and how they interact with whole economy models. It is therefore recommended that:

- The ERP raises awareness of the need for a better understanding of the economic value of low carbon pathways within government and key partners;

- Further work is carried out generally to better understand the gaps in current analysis and the limitations of our ability to assess socio-economic benefits;

- In order to ensure that the limitations of modelling are fully understood, those carrying out modelling works should provide greater transparency regarding modelling input assumptions.

A list of full recommendations include:

- Analysis on economic growth and job creation should be included as part of, or alongside pathway and scenario works wherever possible. This may involve an additional element of secondary analysis.

- Further investigation to consider how models can be used for these assessments is required. This may involve:

  - Reviewing capabilities or key drivers of existing models to provide more definite answers to questions such as: Can current modelling approaches be adapted to assess these impacts in a robust way? And can current models be integrated with other model types to enable these assessments?

  - A greater use of existing ‘top-down’ models;

  - The creation of new models or;

  - The integration of existing model types to enable this kind of analysis and inform policy at a more strategic level. This would ensure a more multiple-perspective approach in regards to modelling of the energy system and help to avoid ‘group-think’.

- It is noted that some ‘E3’ simulation-type models can include a disaggregated ‘bottom-up’ approach to enable assessments of the energy system from both perspectives. Utilisation of these models would help test or validate the outputs of the few existing (UK) models that provide socio-economic assessments, although it is noted that these can have weaknesses too.

- Greater funding support is required for the development of these model types - to improve the quality of outputs and understanding of their potential.

- Clear communication and transparency regarding the design, premise and limitations of modelling works should be encouraged to avoid the risks of misinforming policy, over-interpretation or ‘cherry-picking’.

- Better communication and a wider use of government guidelines for undertaking analysis such as HMT’s ‘Green’, ‘Magenta’ and ‘Aqua’ Books (the latter relating to quality assurance) would ensure a more consistent approach.

- Finally, continued and more detailed work to assess the impacts and benefits of specific technologies for GDP, job creation and investment opportunities is encouraged, including at regional levels. This should involve a deeper analysis of the UK’s potential to capture value from supply chains, plus assessments of international flows and competitiveness of the UK as a ‘region’ within a wider EU/global framework.

## Introduction

Assessments of economic growth and job creation are complex and the associated effects can be difficult to define: “it is due to the non‐market, somewhat intangible nature of socioeconomic benefits, which makes them difficult to quantify”, particularly when attempting to capture the benefits of a single impact, often interlinked with others.

Approaches within pathway and scenario works that do assess these impacts vary greatly. However, in many cases they are not considered at all. The reasons for this are generally related to one, or a selection of the following:

- The intentions or rationale behind the pathways analysis - e.g. designed to highlight future requirements for changes to energy system infrastructure, or to show the least-cost path to 2050;

- The capability of the models used – e.g. the model is not designed for making these kinds of assessments;

- A lack of interest / low priority;

- The modelling approach and quality / accessibility of data – there may be a lack of good quality economic and socio-economic data to base input assumptions on, which is often related to:

  - Uncertainty – there are already a large number of assumptions used as modelling inputs and there can be a reluctance to add more;

  - The somewhat intangible nature of socioeconomic impacts and benefits which makes them hard to define;

  - The sensitive nature of generating outputs that put a figure on economic effects, which may essentially be an estimate and prove contentious (e.g. stating a particular technology’s effects on local GDP).

### Aims and approach

This paper:

- Provides a broad overview of how the UK currently considers and assesses economic impacts and benefits within some of its major pathway and scenario works.

- Checks for consistency in the use of these approaches across relevant scenarios and reports.

- Considers modelling capabilities (now and in future) for making these assessments and highlights other relevant models and works that can assist with analysis in this area.

- Provides a summary of key findings and recommendations for potential future work to be taken forward by other organisations/departments.

The work provides an insight into the types of economic modelling assumptions (inputs) used; highlights the depths of economic analysis (outputs) created; and characterises the models behind the works. A selection of economic-related categories and parameters are shown for illustration purposes.

ERP’s work has been informed by literature reviews, data collection and interviews with pathways and scenarios teams. Additional interviews have taken place with contacts involved in other relevant works such as the Low Carbon Innovation & Coordination Group’s Technology Innovation Needs Assessments (TINAs) and the Sustainable Pathways to Low Carbon Energy (SPLiCE). These are discussed in the ‘Other Relevant Works’ section below.

## Models assessed

The models and associated pathways/scenarios assessed are listed in the table below. These particular models were considered as they have been used to produce five main UK-relevant pathways and scenario works. A definition of ‘pathways’ and ‘scenarios’ can be found in Appendix 3. More detailed summaries of these modelling approaches can be found in Appendix 1.

| Organisation | Model(s) | Associated Pathway(s) / scenarios works of relevance | Timeline of pathways produced | Date of publication | Modelling Approach |
| --- | --- | --- | --- | --- | --- |
| CCC | N/A | CCC’s Fourth Carbon Budget Review, Parts 1&2 | 2050 | June 2011 & December 2013 | Strategic |
| DECC | 2050 Pathways Calculator (and Dynamic Dispatch Model (DDM) as extra analysis) | 2050 Pathways Analysis | 2050 | July 2010 | DECC 2050 Pathways: Democratic DDM: Deterministic (and stochastic) |
| ETI | ESME | Used by DECC to inform its decisions on carbon budgets and the UK carbon plan 1 | Various | N/A | Bottom-up, probabilistic, cost optimisation (to achieve carbon targets) also spatial |
| National Grid | RESOM (post-2035) (pre-2035 as extra analysis) | Future Energy Scenarios (FES) – RESOM model used for post 2035 only | 2050 | July 2013 | Post-2035 – Cost Optimisation (to achieve carbon targets), Bottom-up Pre-2035 Deterministic, Democratic & Econometric |
| UKERC | MARKAL ELASTIC DEMAND (MARKAL-MACRO as extra analysis) | Energy 2050 - Making the Transition to a Secure Low-Carbon Energy System and The UK energy system in 2050: Comparing Low-Carbon, Resilient Scenarios | 2050 | 2010 & February 2013 | MARKAL ELASTIC DEMAND: multi-time period linear, Bottom-up, Cost Optimisation (to achieve carbon targets) model MARKAL MACRO: Econometric, top-down |

A number of other models have been developed by government, industry and academia to address specific areas of interest. There are too many to list within this paper but examples are provided below. The ERP recommends that these (and others), be considered by government in more detail to assess possible interactions between the models (including those considered within this paper), and how they inform policy.

There are a number of additional factors not fully assessed within this paper that should also be considered in future analysis. These include:

- Assessments of fuel poverty

- More in-depth analysis regarding regional effects

- Analysis of economic distributional effects and

- Value capture, supply chains and flows within the UK economy.

A range of model classifications relating to the ‘Modelling Approach’ column in the table above are defined in the lists below. These lists are not exhaustive but help to define the models assessed.

# Model classifications

# To add to the IPCC definitions on page 4, two main and broad classifications as noted by the ETI are listed below, although it is noted that definitions can vary and many other types can exist within these:

- Bottom-up: optimisation models are referred to as bottom-up models because they consider specific technical opportunities and their energy, cost and emission implications. In bottom-up models (such as ESME) the macro-economy is not modelled but is usually represented via exogenous assumptions derived from other works.

- Top-down: in contrast to bottom-up models, top-down models analyse aggregate behaviour using historically derived economic trends. Top-down models are more suitable for studying economy-wide responses to energy policies and other drivers, and can generate insights into income, GDP, and economic competitiveness. However, technological detail and real-world constraints are generally aggregated and hence not modelled in detail. Top-down models include computable general equilibrium (CGE) models and macro- econometric models such as The Cambridge Econometric’s MDM-E3 model, and have been widely used to study economy-wide effects of energy policies and the transition to a low-carbon economy.

However, some top-down models such as the aforementioned MDM-E3 (a macro-simulation model), are able to incorporate a bottom-up approach also, enabling analysis of the energy system within a UK macro-economic context i.e. the model enables assessments of job creation, GDP and supply chain impacts at an energy sector or technology-based level.

It is important to note that although this study has assessed modeling capabilities in relation to economic impacts, it hasn’t necessarily assessed the robustness of these capabilities.

Other model types include: Strategic (termed by ERP): pathways are developed based on outputs from a range of models, where the type of model used is selected based on its suitability to model the sector and answer the research question; pathways are further informed by judgment to address considerations outside the scope of available models, such as creating technology options for the future, achieving market uptake, etc. Democratic (termed by DECC/ERP): involves stakeholder participation/interaction. E.g. National Grid consults a wide range of stakeholders to inform its modeling inputs and outputs and to create axioms and DECC’s 2050 Calculator allows users of the tool to explore their own choices. Deterministic: every set of variable states is uniquely determined by parameters in the model and by sets of previous states of these variables. Therefore, deterministic models perform the same way for a given set of initial conditions. Stochastic/ Probabilistic: contrasts a deterministic model. Randomness is present and variable states are not described by unique values, but rather by probability distributions. ETI’s ESME model accounts for uncertainty using a probabilistic approach based on Monte Carlo simulations. Cost optimisation: programmed to always select the least-cost path but can have added or secondary constraints e.g. least-cost path to meeting the carbon targets. Examples are MARKAL which is a multi-time period linear cost optimisation model and the RESOM model (used with National Grid), which is also a cost-optimisation model. Econometric / macro-economic: designed to examine the dynamics of aggregate quantities such as the total amount of goods and services produced, total income earned, the level of employment of productive resources, and prices etc. Macroeconomic models may be logical, mathematical and/or computational and are often described as top-down models (see above), although there can be a number of other classifications within these. MARKAL-Macro is a hybrid energy systems/macroeconomic model that was used to calculate the impact of decarbonisation on UK GDP growth. Spatial: often top-down and include any of the formal techniques that study entities using their topological, geometric, or geographic properties. MARKAL has a spatial version, which is a multi-region model of the UK to explicitly analyse new supply-demand-infrastructure combinations. It is a ‘2-region’ model to examine devolved Scottish energy policy. The ESME model is spatially disaggregated (12 onshore nodes, 2 carbon storage nodes, 9 offshore nodes) to take account of the variation in resource supply and demand across the UK. Integrated Assessment: these models are commonly used in studies (including The Stern Review) to determine the social cost of carbon, and (rarely) in cost-benefit analyses to determine “optimal” climate change policy, e.g. for informing the setting of targets. Computable General Equilibrium (CGE): CGE top-down models offer a comprehensive way of modeling the overall impact of policy changes on the economy. They are completely specified models of an economy or a region, including all production activities, factors and institutions, and including the modeling of all markets and macroeconomic components, such as investment and savings, balance of payments, and government budget. These models incorporate many economic linkages and can be used to try to explain medium to long-term trends and structural responses to changes in development policy. Partial Equilibrium: In contract to CGE models, partial equilibrium models treat one particular sector of the economy as operating in isolation from the other sectors of the economy. Most of the approaches of the models/works assessed within this paper are partial equilibrium models and assess the energy system or one particular sector only.

## Comparison of the Pathways

The table below provides a summary of model classifications. As highlighted above, the models required for assessing economic and socio-economic impacts are predominantly econometric / macro-economic (top-down) and spatial models. Of those assessed in this paper, there is a lack of these modelling approaches (ticks in brackets mean partially).

Summary tables 1, 2 & 3 below highlight consistencies or inconsistencies relating to input assumptions, methodologies and outputs for assessing economic and socio-economic impacts. The tables show a selection of results from the economic categories and parameters used to compare modelling approaches and capabilities.  Links to online full detailed ‘assessment’ tables, with responses from each of the pathways and scenario teams can be found in Appendix 2. These have been structured in the following way, with a glossary of parameters and terms used found in Appendix 3:

- Table 1 – Inputs & Outputs: assesses the use of a range of economic modelling inputs and associated outputs

- Table 2 - Methodology & Outputs: describes the methodologies of the pathways/scenarios works informed by the models and asks more qualitative questions relating to outputs, plus dependencies on other models.

- Table 3 - Modelling capabilities: captures the capabilities of the models for carrying out future economic value and impact assessments.

### Modelling inputs

Table 1 shows that few of the models are able to provide the outputs sought in this paper. Although they use a wide range of modelling inputs, these types of input assumptions (such as GDP or investment rates) are often required to inform other parameters within the model e.g. total amounts for demand or effects on build rates. However, the use of these parameters varies per model depending on what it’s been designed to achieve, which therefore determines whether the input is required.

There is some consistency noted regarding the figures used as inputs. Figures for discount rates, for example, are often sourced from HMT’s Guidance ‘The Green Book’ (summarised below), but other input figures vary and are taken from a range of sources and approaches. An instance of this is the use of ‘hurdle rates’ (defined in Appendix 3) in relation to discount or investment rates. MARKAL uses some technology-specific discount rates in the form of hurdle rates to reflect consumer behaviour, and DECC’s DDM uses hurdle rates to reflect investment rates.

Table 2 provides further detail regarding the models’ approaches and methodologies and summarises the reasons for carrying out the assessments. These vary but tend to be focused on cost-optimisation with meeting carbon targets as a secondary constraint. The table additionally provides information about model dependencies and influences on other pathway and scenario works.

### Model outputs

Results relating to analysis of the selected output parameters in table 1 are ‘patchier’ and where these have been assessed; there are often caveats where only part of the impact has been considered.

Of the models evaluated, ESME is the only model with capability to analyse regional job creation, although this is carried out as secondary analysis and inferred from a related output result e.g. total amounts of onshore wind deployed within twelve UK regions on a five-yearly basis.

In regards to effects on GDP, relatively few models make this kind of output assessment. The CCC aggregates the costs of measures to reduce GHG emissions in their fourth carbon budget scenario to determine the overall cost to GDP. ‘The analysis is based on a ‘resource cost’ methodology (i.e. it sums the direct additional costs of implementing measures in CCC scenarios to reduce emissions). This reflects the findings of previous work using HMRC’s general equilibrium model and Cambridge Econometrics’ macro-econometric model, that a resource cost estimate is likely to capture the most important elements of the GDP cost’.

DECC / HMG have used the HMRC model to produce an explicit GDP figure for the 4th Carbon Budget analysis, published in the Carbon Plan. The macroeconomic impact of meeting the budget is estimated at an average cost of 0.6% of GDP a year over the 4th carbon budget period (while noting that macro models generally don’t account for benefits such as the avoided costs of climate change – estimated as 5-20%+ of GDP in The Stern Review). Cambridge Econometrics’ MDM-E3 model has also just been used for this purpose, finding a positive GDP impact.

It is therefore important to focus on what the models have been used for when attempting to measure impacts on GDP (i.e. it’s generally the impact of specific targets (e.g. the 4th Carbon Budget), relative to a ‘no action’ baseline). This poses the question of whether certain models can be adapted to measure effects such as economic growth and job creation more generally.

Table 3 provides an overview of the capabilities of the models considered. Information from table 1 is included for reference. Where a selected parameter is not currently assessed, the question is raised as to whether the model could be adapted to assess it in future. For reasons noted above relating to the original premise of the models, the answer to this question is often ‘no’. There is a perception that this type of analysis would add to uncertainty and be too complex to assess (possibly true within the models considered). However there is also some ambiguity regarding modelling capabilities (cells left blank or responses of ‘not sure’). This additionally comes across in conversations with contacts from modelling teams, some feel a form of integration could be achieved and would be useful, others disagree.

### Potential from other modelling approaches

Although not fully assessed as part of this work, it is worth noting that the MARKAL-MACRO model can assess effects on GDP/GVA but not job creation. Similarly, other models such as DECC’s DDM and MARKAL look at welfare impacts which is being increasingly considered. The results in table 1 highlight the gaps in analysis relating to economic and socio-economic outputs as part of current modelling approaches.

Please zoom in to view tables more clearly (200%)

## Use of Government Guidelines

Three main sets of existing guidelines (produced by UK Government) for assessing economic value and benefits within projects and policies currently exist – these are detailed in Appendix 4. Analysis shows some use of these guidelines, mainly for discount rates (HMT guidance recommends a figure of 3.5% here) but despite an overall awareness, consistency in their use is variable.

Areas for consideration are better communication of, or encouragement for the use of guidelines such as these; or more specific guidelines aimed at those carrying out energy-system modelling and analysis. These guidelines could detail the economic, socio-economic (and other) aspects of analysis that government is particularly interested in and how to carry out these assessments.

## Job creation and value capture of supply chains

Although greater analysis of socio-economic impacts such as job creation (at net and regional levels) is recommended within this paper, it is noted that this is one of the more complex effects to assess. The works of Fankhauser et al. (2008) and Kammen et al. (2006) discuss the direct effect, the dynamic effect and total employment. Factors such as ‘mismatch’ between old and new jobs or ‘displacement’ requires consideration and adds to the difficulties of capturing the overall impacts. The issues of Global Value and Supply Chains (discussed by Dedrick et al, 2008 and the OECD ‘Mapping Global Value Chains’, 2012, for example) add additional complexities

There are a number of existing studies that assess the economic impacts of particular energy technologies such as ‘The economic benefits of CCS in the UK’ (CCSa & TUC), which shows the potential GVA added, the potential number of jobs created and effects on GDP. However, a great deal of uncertainty continues to surround discussions of job creation: ‘Although there are opportunities in the transition (to a low carbon economy), it is not clear to what extent low carbon jobs will be additional to existing jobs’ and, ‘in the long run, arguments that improvements in environmental quality can “create” jobs should not be taken to mean that such improvement can increase total employment’. More detailed assessments perhaps incorporated within pathway and scenario works would be of value here.

Internal working guidance in DECC notes that job estimates must be estimated on a consistent basis with clear descriptions of what the estimates represent and recognising the issue of gross vs. net jobs.

Finally, more detailed assessments of the UK as a ‘region’ within a wider EU/global framework would be beneficial, particularly to assess capital flows, supply chains and value capture (e.g. investment and financing from outside the UK, with macroeconomic implications).

## An overview of other relevant works

There are a number of additional works that assess or discuss the types of impacts considered within this paper. A selection of these are:

- The Low Carbon Innovation and Coordination Group’s (LCICG) Technology Innovation Needs Assessments (TINAs) which include estimates of the effects of low-carbon technologies on UK GDP from an innovation perspective. The purpose of the TINAs is to ‘inform government decisions by providing a robust and consistent evidence base on the innovation needs of technologies likely to be important in delivering the UK’s energy and climate change targets and/or economic benefits across low carbon technologies’. In order to provide these estimates, methodologies for how to assess the value of learning rates and for assessing the value in business creation have been included as part of the work.

- The forthcoming Sustainable Pathways to Low Carbon Energy (SPLiCE) programme which will look specifically at the impacts of different energy technologies on the natural environment, society and the economy. SPLiCE is a 3-5 year collaborative UK research programme which aims to fill significant gaps in knowledge about the sustainability of different mixes of energy supply and demand options needed to deliver 2050 greenhouse gas UK emissions targets. It will look specifically at the impacts of different energy technologies on the natural environment, society and the economy. This new research will be combined with existing information and synthesised into a comprehensive, accessible and holistic view of the data that will support decision making to build a sustainable future energy system.

- The BIS Industrial Strategies, as their approach is based on ‘identifying where the UK can have greatest success in capturing high value opportunities based on its key strengths and capabilities.’ Better assessments of economic and socio-economic impacts can help with identifying these areas i.e. the pathways and technologies that will have the greatest benefits and investment/supply chain opportunities.

- DECC’s Updated Energy Projections (UEPs) which are published every year and provide updated energy projections analysing and projecting future energy use and greenhouse gas emissions in the UK. These projections allow progress monitoring for meeting the UK’s carbon budgets and are used to inform energy policy and associated analytical work across government departments. The projections are based on assumptions of future economic growth, fossil fuel prices, electricity generation costs, UK population and other key variables regularly updated. They also give an indication of the impact of the uncertainty around some of these input assumptions. https://www.gov.uk/government/collections/energy-and-emissions-projections

- Work by Siemens, who have performed a macro-economic analysis on electricity generation costs with a concept called “SCOE – Society‘s cost of Electricity“. The analysis is looking beyond LCOE (levelised cost of energy) and takes a bigger scope of costs related to power generation into account – namely transmission costs, variability costs, subsidies, social costs, employment and economic effects and geopolitical costs.

- The Royal Academy of Engineering have previously looked at the physical assets required for the transformation of the energy system to 2050, based on what some modelling outputs are suggesting and whether it is feasible to deliver them. There is agreement of the need to include practicalities and supply chain issues within modelling analysis.

Finally, the ongoing works of departments, organisations and institutes to develop modeling capabilities, ensure quality assurance and facilitate/look into modelling integration are of importance. These are also perhaps channels by which some of the messages from this paper can be incorporated. Examples of these are:

- The UCL Bartlett Institute & wholeSEM Consortium’s work to define existing modelling types, map UK modelling expertise and look at which models do (or can be) linked.

- UKERC’s upcoming work to look at integrating models and developing links between energy systems and macro-economic models.

## Conclusions

- There are a variety of model types and approaches used to produce current UK pathways and scenarios analysis, but with a definite focus on 1) cost-optimisation and 2) how to achieve carbon targets (i.e. what is affordable/practical and physically deliverable). Feedback from the relevant teams has shown that the models assessed have been created with the above goals in mind and constraints are set around them. Unsurprisingly, these are areas of great importance and interest, but the approach taken potentially limits the models’ abilities to assess additional factors, such as economic and socio-economic impacts.

- On the whole, assessments of the economic and socioeconomic impacts of low carbon pathways have been relatively neglected, although it is accepted that these are complex to measure and define. ‘Formal modelling of the overall impact of climate change in monetary terms is a formidable challenge’. There are limitations to modeling which ’demands great caution in interpreting results’.

- From the models assessed, there is a lack of UK ‘top-down’ and ‘spatial’ modelling approaches being utilised to inform pathway and scenario works to generate modelling outputs for impacts such as economic growth and job creation.

- These types of models do exist (e.g. the Cambridge Econometrics’ MDM-E3) but many are not set up to assess the economic value of low carbon pathways and the range of economic and socio-economic impacts of interest to policy-makers.

- Where economic impacts such as effects on jobs, supply chains and local GDP are assessed, they are often discussed within texts in a general and qualitative fashion. Works that previously carried out these assessments have adopted other, less detailed approaches, or have reduced this type of analysis substantially. This is largely to avoid introducing further uncertainty amongst input assumptions or because research interests lie elsewhere.

- From those assessed, ETI’s ESME model is the only model with a capability for assessing potential job creation in relation to regions, but this is carried out as secondary analysis (i.e. inferred from the results) and is not a direct output from the model.

- There are a number of economic inputs utilised within the modelling approaches. Most of the models assessed include all or a mixture of the following (as shown in the tables above): An exogenous amount for GDP, figures for CAPEX & OPEX, discount rates, assumptions around investment/build rates and learning rates but the types of inputs selected very much depend on what the model is trying to achieve and determine the outputs produced.

- Modelling outputs are therefore reliant on associated inputs - therefore the type and quality of assumptions will affect the modelling results. In the context of cost-optimisation models, input figures for capex and opex per technology (for example) will affect how much of a particular technology is deployed within the analysis. As this could potentially have an effect on action taken (and on supply chains etc.), it is important to have clarity and consider the sources of these input assumptions.

- There is some consistent use of government guidelines e.g. figures for social discount rates as stated in HMT’s Green Book guidelines, but other input figures vary and are taken from a range of sources and approaches.

- Responses show that in many cases, assessing these economic impacts ‘is not within the premise of the work’ and existing models cannot be easily adapted to address them. However, there is a level of ambiguity surrounding this. It is possible to combine model types to produce this type of analysis, as long as aims are well defined and modelling limitations are made clear.

## Recommendations

This study has looked at a variety of models and criteria used to make judgements about future low carbon pathways and potential benefits to the UK. It is clear that further work is required to better understand the full range of models available in government, industry and academia to support this assessment, their limitations and how they interact with whole economy models. It is therefore recommended that:

- The ERP raises awareness of the need for a better understanding of the economic value of low carbon pathways within government and key partners;

- Further work is carried out generally to better understand the gaps in current analysis and the limitations of our ability to assess socio-economic benefits;

- In order to ensure that the limitations of modelling are fully understood, those carrying out modelling works should provide greater transparency regarding modelling input assumptions.

A list of full recommendations include:

- Analysis of economic growth and job creation should be included as part of, or alongside pathway and scenario works wherever possible. This may involve an additional element of secondary analysis.

- Further investigation to consider how models can be used for these assessments is required. This may involve:

  - Reviewing capabilities or key drivers of existing models to provide more definite answers to questions such as: Can current modelling approaches be adapted to assess these impacts in a robust way? And can current models be integrated with other model types to enable these assessments?

  - A greater use of existing ‘top-down’ models;

  - The creation of new models or;

  - The integration of existing model types to enable this kind of analysis and inform policy at a more strategic level. This would ensure a more multiple-perspective approach in regards to modelling of the energy system and help to avoid ‘group-think’.

- It is noted that some ‘E3’ simulation-type models can include a disaggregated ‘bottom-up’ approach to enable assessments of the energy system from both perspectives. Utilisation of these models would help test or validate the outputs of the few existing (UK) models that provide socio-economic assessments, although it is noted that these can have weaknesses too.

- Greater funding support is required for the development of these model types - to improve the quality of outputs and understanding of their potential.

- Clear communication and transparency regarding the design, premise and limitations of modelling works should be encouraged to avoid the risks of misinforming policy, over-interpretation or ‘cherry-picking’.

- Better communication and a wider use of government guidelines for undertaking analysis such as HMT’s ‘Green’, ‘Magenta’ and ‘Aqua’ Books (the latter relating to quality assurance) would ensure a more consistent approach.

- Finally, continued and more detailed work to assess the impacts and benefits of specific technologies for GDP, job creation and investment opportunities is encouraged, including at regional levels. This should involve a deeper analysis of the UK’s potential to capture value from supply chains, plus assessments of international flows and competitiveness of the UK as a ‘region’ within a wider EU/global framework.

## Next steps /considerations

This paper will be circulated amongst relevant organisations with an interest or the potential to act upon its findings. These include: UK pathway, scenario and modelling teams, the Energy Systems Catapult, the WholeSEM Consortium and HMT.

Following this scoping work, ERP recommends:

- A review of existing UK modelling capabilities for carrying out robust analysis relating to economic growth and job creation from low carbon pathways. This should include an assessment of potential modelling adaptation or integration opportunities and should be led by an expert body with capability to look across the whole system, such as the Energy Systems Catapult or the WholeSEM Consortium, with accountability to government.

- Those carrying out modelling, pathway and scenario works should ensure greater transparency regarding input assumptions to avoid misinforming policy. Policy makers must be aware of the limitations of individual models.

- Pathway and scenario models should ideally be ‘housed’ within independent or impartial organisations to help enable transparency.

- Pathway and scenario teams should, wherever possible, include assessments of economic growth and job creation as part of modelling works, even in the form of supplementary or secondary analysis.

- Better communication and a wider use of existing government guidelines for undertaking analysis such as HMT’s ‘Green’, ‘Magenta’ and ‘Aqua’ Books (the latter relating to quality assurance) to ensure a more consistent approach.

- Government and The Research Councils should provide greater funding to enable this type of analysis and additionally for the creation of new models / teams (where required).

## Acknowledgements

# ERP would like to thank the members of the project steering group, interviewees - including contacts from modelling, pathways and scenarios teams, and contacts from the LCICG TINAs and SPLiCE programmes for their input to this project work.

# EVAP Steering Group:

# Chris Pook (BIS) – Steering Group Chair

# Tom Delay (The Carbon Trust)

# Rob Saunders (TSB)

# Will Lecky (DECC)

# Emma Edworthy (Welsh Government)

# James Bolton / Aftab Malik (BIS)

# Kenny Richmond (Scottish Enterprise)

# Eric Ling (CCC)

# Footnotes

Top-down and bottom-up models are defined by the IPCC and these definitions are used within this paper: “Top-down and bottom-up models are the two basic approaches to examine the linkages between the economy and specific GHG emitting sectors such as the energy system. Top-down models evaluate the system from aggregate economic variables, whereas bottom-up models consider technological options or project-specific climate change mitigation policies. IPCC SAR on economic & social dimensions (IPCC, 1996a, Chapter 8) includes an extensive discussion on the differences between top-down and bottom-up models. It concludes that the differences between their results are rooted in a complex interplay among the differences in purpose, model structure and input assumptions (IPCC, 1996a, Section 8.4.3).  www.ipcc.ch/ipccreports/tar/wg3/index.php?idp=310

“There are valuable opportunities for British businesses to develop and manufacture these products [technologies to help decarbonize], for both domestic and international consumption… Although there are opportunities in the transition, there would also be costs on business, and it is not clear to what extent low carbon jobs will be additional to existing jobs.” (DECC’s 2050 Pathways Analysis, July 2010 – page 12: Understanding the role of the economy in the pathways).

National Grid previously carried out economic analysis within their Future Energy Scenarios (FES) work but have reduced this over time to avoid additional uncertainties regarding input assumptions.

http://www.iea.org/publications/insights/ee_improvements.pdf Exec Sum page 3

http://www.carbontrust.com/resources/reports/technology/tinas-marine-energy,-carbon-capture,-heat,-bioenergy,-electricity-networks-and-storage

http://www.lwec.org.uk/sustainable-pathways-low-carbon-energy

Information regarding National Grid’s RESOM (Redpoint Energy System Optimisation Model – post 2035) has been provided by the scenarios team for assessment as part of this work. Information regarding the (multiple) modelling techniques used pre-2035 are complex, therefore information regarding these approaches is included in Appendix 1D.

NB there are a number of versions of the MARKAL model, including two versions relevant to this paper: MARKAL ELASTIC DEMAND and MARKAL-MACRO  - an overview of both models are included in Appendix 1E.

Source: Modelling Low-Carbon Energy System Designs with the ETI ESME Model, Chris Heaton, Strategy Manager – Modelling, ETI, April 2014

An axiom is a premise or starting point of reasoning. It is a logical statement assumed to be true.

https://www.gov.uk/government/uploads/system/uploads/attachment_data/file/68816/216-2050-pathways-analysis-report.pdf

Source: World Bank  http://web.worldbank.org/WBSITE/EXTERNAL/TOPICS/EXTPOVERTY/EXTPSIA/0,,contentMDK:20481443~menuPK:1108016~pagePK:148956~piPK:216618~theSitePK:490130~isCURL:Y,00.html

http://www.businessdictionary.com/definition/partial-equilibrium-analysis.html

http://archive.theccc.org.uk/aws3/TSO-ClimateChange.pdf

The Stern Review, 2006 http://webarchive.nationalarchives.gov.uk/+/http:/www.hm-treasury.gov.uk/independent_reviews/stern_review_economics_climate_change/stern_review_report.cfm

16. Using today’s most common shorthand of national welfare, gross domestic product), all of the above [$10 million spent constructing a jail, $10 million spent producing a line of smartphones, $10 million clear-cutting rain forests to produce $10 million in lumber and $10 million in storm repairs], are equal. GDP measures only output, and makes no claims on the quality of that output, let alone on subjective concepts such as social progress or human happiness…this is why more and more economists and activists are pushing to update GDP [goes on to suggest guidelines for doing so]. Source: BllombergView (online) – GDP: An Imperfect Measure of Progress, Jan 30 2013 (by the Editors) www.bloombergview.com/articles/2013-01-30/gdp-an-imperfect-measure-of-progress

Bowen, A., Fankhauser, S., The green growth narrative: Paradigm shift or just spin?. Global Environ. Change, 2011

Report of the Renewable and Appropriate Energy Laboratory Putting Renewables to Work: How Many Jobs Can the Clean Energy Industry Generate? Daniel M. Kammen et al of the Energy and Resources Group Goldman School of Public Policy, April 2004 (corrected 1/31/06)

which depends on the labour intensity of the industry concerned

which relates to the innovation that occurs as new technologies are developed, adapted to and exploited, increasing productivity and therefore economic output.

It is raised that net effects on total employment depend on where the additional labour is drawn from (the employed or unemployed) and if that labour is drawn from the employed, whether the labour required to fill the newly vacated jobs will be drawn from the employed or unemployed, and so on.

Who Profits from Innovation in Global Value Chains? A Study of the iPod and notebook PCs, Dedrik et al 2008

Mapping Global Value Chains OECD, 2012

The economic benefits of carbon capture and storage in the UK, CCSa & TUC 2013

based on the ‘achievable aspiration of 75% UK supply chain content’

DECC’s 2050 Pathways Analysis & Calculator, July 2010: https://www.gov.uk/government/uploads/system/uploads/attachment_data/file/68816/216-2050-pathways-analysis-report.pdf

TINA Methodology slide-pack

Estimation of the value in business creation takes a ‘top down’ look at the potential global market for the technology and attempts to quantify the potential value which could be captured by the UK economy (TINA methodology overview slide-pack).

SPLiCE website: http://www.lwec.org.uk/sustainable-pathways-low-carbon-energy

BIS Industrial Strategy: UK Sector Analysis, Sept 2012 https://www.gov.uk/government/uploads/system/uploads/attachment_data/file/34607/12-1140-industrial-strategy-uk-sector-analysis.pdf

The whole systems energy modelling consortium (wholeSEM) is a £5.7 million initiative to develop, integrate and apply state-of-the-art energy models. wholeSEM consists consortium is made up of: EPSRC, University of Surrey, UCL, University of Cambridge and Imperial College.

http://webarchive.nationalarchives.gov.uk/20130129110402/http://www.hm-treasury.gov.uk/d/Executive_Summary.pdf

There are valuable opportunities for British businesses to develop and manufacture these products [technologies to help decarbonize], for both domestic and international consumption… Although there are opportunities in the transition, there would also be costs on business, and it is not clear to what extent low carbon jobs will be additional to existing jobs. (DECC’s 2050 Pathways Analysis, July 2010 – page 12: Understanding the role of the economy in the pathways).

National Grid previously carried out economic analysis within their  Future Energy Scenarios (FES) work but have reduced this over time to avoid additional uncertainties regarding input assumptions.